## Slide 1: Exercise: Organizing, Loading, and Publishing Point Observations Using HydroServer
Support
EAR 0622374
CUAHSI
HIS
Sharing hydrologic data
http://his.cuahsi.org/
Jeffery S. Horsburgh
David G. Tarboton, Kimberly A. T. Schreuders, David R. Maidment, Ilya Zaslavsky, and David Valentine
And the Rest of the CUAHSI HIS Team

## Slide 2: In this Exercise
GOAL: Publish observational data for a site in the Little Bear River using HydroServer in about an hour
HydroServer Training Machine
  http://hydroserver.uwrl.usu.edu
  Windows Server 2008 R2
  Microsoft SQL Server 2008 R2
  HydroServer Software (ODM Tools and data loaders)

## Slide 3: The Data You Will be Using
7 water quality and streamflow monitoring sites
  Temperature
  Dissolved Oxygen
  pH
  Specific Conductance
  Turbidity
  Water level/discharge
2 weather stations
  Temperature
  Relative Humidity
  Solar radiation
  Precipitation
  Barometric Pressure
  Wind speed and direction
Spread spectrum radio telemetry network

## Slide 4: Publish Point Observations
Create an ODM database
  Load site, variable, method, and source information using the ODM Data Loader
  Load observations using the ODM Streaming Data Loader
Visualize and explore the data using ODM Tools
Publish the data by creating a WaterOneFlow web service

## Slide 5: ODM Data Loader
Loading data to any table in ODM – e.g., Sites, Variables, Methods, etc.
Loading Data Values in serial format
  Multiple sites and variables in one file
  All data values in a single column
Site | Variable | Date | Value
1 | Temperature | 8/2/2007 14:00 | 12.4
1 | Temperature | 8/2/2007 14:30 | 12.7
1 | Temperature | 8/2/2007 15:00 | 13.1
… | … | … | …
1 | Dissolved Oxygen | 8/2/2007 14:00 | 9.78
1 | Dissolved Oxygen | 8/2/2007 14:30 | 9.70
1 | Dissolved Oxygen | 8/2/2007 15:00 | 9.56
… | … | … | …
2 | Specific Conductance | 8/2/2007 14:00 | 351.7
2 | Specific Conductance | 8/2/2007 14:30 | 350
2 | Specific Conductance | 8/2/2007 15:00 | 351.2

## Slide 6: ODM Streaming Data Loader
Focused on loading data values
Crosstab data
  Single site, multiple variables
  Date in one column, each variable in one column
  Datalogger files from field sensors
Date | Variable_1 | Variable_2 | … | Variable_n
8/2/2007 14:00 | 13.01298 | 1.155137 | … | 9.391667
8/2/2007 14:30 | 13.222 | 1.15333 | … | 9.586666
8/2/2007 15:00 | 13.19934 | 1.153291 | … | 9.75
8/2/2007 15:30 | 13.19094 | 1.153561 | … | 9.78
8/2/2007 16:00 | 13.17751 | 1.16075 | … | 9.703334
… | … | … | … | …

## Slide 7: Questions?
Support
EAR 0622374
CUAHSI
HIS
Sharing hydrologic data
http://his.cuahsi.org/