## Slide 1: Exercises: Organizing, Loading, and Managing Point Observations Using HydroServer
Support
EAR 0622374
CUAHSI
HIS
Sharing hydrologic data
http://his.cuahsi.org/
Jeffery S. Horsburgh
Utah Water Research Laboratory
Utah State University

## Slide 2: In this Exercise
GOAL: Organize and load observational data for a continuous water quality monitoring site in the Little Bear River
Training Machine Software
  Microsoft SQL Server 2008 R2 Express
  CUAHSI HIS ODM Data Loader
  CUAHSI HIS ODM Streaming Data Loader
  CUAHSI HIS ODM Tools

## Slide 3: The Data You Will be Using
7 water quality and streamflow monitoring sites
  Temperature
  Dissolved Oxygen
  pH
  Specific Conductance
  Turbidity
  Water level/discharge
2 weather stations
  Temperature
  Relative Humidity
  Solar radiation
  Precipitation
  Barometric Pressure
  Wind speed and direction
Spread spectrum radio telemetry network

## Slide 4: Steps
Create an ODM database
  Load site, variable, method, and source information using the ODM Data Loader
  Load observations using the ODM Streaming Data Loader
Visualize and explore the data using ODM Tools

## Slide 5: ODM Data Loader
Loading data to any table in ODM – e.g., Sites, Variables, Methods, etc.
Loading Data Values in serial format
  Multiple sites and variables in one file
  All data values in a single column
Site | Variable | Date | Value
1 | Temperature | 8/2/2007 14:00 | 12.4
1 | Temperature | 8/2/2007 14:30 | 12.7
1 | Temperature | 8/2/2007 15:00 | 13.1
… | … | … | …
1 | Dissolved Oxygen | 8/2/2007 14:00 | 9.78
1 | Dissolved Oxygen | 8/2/2007 14:30 | 9.70
1 | Dissolved Oxygen | 8/2/2007 15:00 | 9.56
… | … | … | …
2 | Specific Conductance | 8/2/2007 14:00 | 351.7
2 | Specific Conductance | 8/2/2007 14:30 | 350
2 | Specific Conductance | 8/2/2007 15:00 | 351.2

## Slide 6: ODM Streaming Data Loader
Focused on loading data values
Crosstab data
  Single site, multiple variables
  Date in one column, each variable in one column
  Datalogger files from field sensors
Date | Variable_1 | Variable_2 | … | Variable_n
8/2/2007 14:00 | 13.01298 | 1.155137 | … | 9.391667
8/2/2007 14:30 | 13.222 | 1.15333 | … | 9.586666
8/2/2007 15:00 | 13.19934 | 1.153291 | … | 9.75
8/2/2007 15:30 | 13.19094 | 1.153561 | … | 9.78
8/2/2007 16:00 | 13.17751 | 1.16075 | … | 9.703334
… | … | … | … | …

## Slide 7: Questions?
Support
EAR 0622374
CUAHSI
HIS
Sharing hydrologic data
http://his.cuahsi.org/