## Slide 1: Advancing an Information Model for Environmental Observations
Jeffery S. Horsburgh
Anthony Aufdenkampe, Richard P. Hooper, Kerstin Lehnert, Kim Schreuders, David G. Tarboton
CUAHSI
HIS
Sharing hydrologic data
Support EAR 0622374

## Slide 2: The Original Problem Combining Similar Data from Disparate Sources
request
NWIS
NAWQA
NAM-12
request
request
request
request
request
request
request
request
return
return
return
return
return
return
return
return
Slide from Michael Piasecki
NARR
return

## Slide 3: CUAHSI Hydrologic Information System A Services Oriented Architecture for Sharing Hydrologic Observations
Slide from Steven Brown

## Slide 4: Point Observations-Network Information Model
A data source operates an observation network
A network is a set of observation sites
A site is a point location where one or more variables are measured
A variable is a property describing the flow or quality of water
A value is an observation of a variable at a particular time
A qualifier is a symbol that provides additional information about the value
Data Source
Network
{Value, Time, Qualifier}
USGS NWIS
NWIS Sites
San Marcos River at Luling, TX
Discharge
18,700 cfs, 3 July 2002
Sites
Variables
Observation

## Slide 5: Data Values – Indexed by “What-Where-When”
Space, S
Time, T
Variables, V
s
t
Vi
vi (s,t)
“Where”
“What”
“When”
A data value

## Slide 6: Data Series – Time Series of Data Values
Space
Variable, Vi
Site, Sj
End Date Time, t2
Begin Date Time, t1
Time
Variables
Count, n
There are n measurements of Variable Vi at Site Sj from time t1 to time t2

## Slide 7: Observations Data Model (ODM)
Soil
moisture
data
Streamflow
Flux tower data
Groundwater
levels
Water Quality
Precipitation
& Climate
A relational database at the single observation level
Metadata for unambiguous interpretation
Traceable heritage from raw measurements to usable information
Promote syntactic and semantic consistency
Horsburgh, J. S., D. G. Tarboton, D. R. Maidment, and I. Zaslavsky (2008), A relational model for environmental and water resources data, Water Resources Research, 44, W05406, doi:10.1029/2007WR006392.

## Slide 8
Set of query functions
Returns data in WaterML
WaterML and WaterOneFlow
WaterML is an XML language for communicating water data
WaterOneFlow is a set of web services based on WaterML
Notes: 8

## Slide 9: HydroCatalog http://hiscentral.cuahsi.org
Metadata Catalog Database
Hydrologic Concept Ontology
Data Discovery Web Services
Service registry
Metadata harvester
Catalog database
Semantic tagging application
Data discovery services

## Slide 10: Thematic keyword search
Integration from multiple sources
Search on space and time domain
HydroDesktop – Data Access and Analysis

## Slide 11: A Common Information Model Has Enabled
A greater degree of semantic and syntactic homogeneity across data sources
Ability to catalog and provide semantically enabled search services across multiple disparate data sources
Evolution toward community standards for sharing hydrologic data

## Slide 12: Limitations
Works great for a limited class of hydrologic observations (e.g., point time series), BUT…
  Does not adequately support some types of ex situ observations
  Does not adequately support observations on geometries other than points
  Does not adequately describe the “feature of interest” or the “sampled feature” or “Site Type”
  Does not provide adequate ability to record provenance and annotate observations
  …

## Slide 13: Critical Zone Research
http://criticalzone.org/Research.html
Soil moisture
Groundwater levels
Streamflow
Stream chemistry
Groundwater chemistry
Soil chemistry
Solid earth chemistry
Precipitation
Both in situ and ex situ data are critical for analysis of the critical zone.

## Slide 14: Coupled Human/Natural Systems
Snow depth, distribution, density
Precipitation
Groundwater withdrawal, recharge, quality
Irrigation, Evapotranspiration
Diversions, human water management
Reservoir inflows, storage, releases
Streamflow quantity, quality
Data representing multiple hydrologic features with complex geometries.

## Slide 15: A More Flexible Information Model for Observations
A number of important advancements have emerged
  Information Model
    Open Geospatial Consortium Observations & Measurements
  Service Interfaces
    Open Geospatial Consortium Standards – particularly Sensor Observation Services (SOS)
  Semantics and Integration
    Scientific Observations Network (SONet)
  Data Storage Model
    Microsoft Research and SDSC Environmental Data Model (EDM)

## Slide 16: International Standardization of WaterML
Hydrology Domain Working Group
- working on WaterML 2.0
- organizing Interoperability Experiments focused on different sub-domains of water
- towards an agreed upon feature model, observation model, semantics and service stack
http://external.opengis.org/twiki_public/bin/view/HydrologyDWG/WebHome
Iterative Development
Timeline
Groundwater IE
  GSC+USGS
  Dec 09 – Dec 10
Surface Water IE
  CSIRO+many
  Jun 10 – Sep 11
Forecasting IE
  NWS+Deltares?
  Sep 11 – Sep 12?
Water Quality IE
Water Use IE
WaterML 2 SWG
(Mar 2011)
June’11
Slide from Ilya Zaslavsky

## Slide 17: ODM 2.0
Approach: a core observational data model with flexible extensions
  Samples extension – better handle storage of sample information and observations derived from ex situ analyses
  Field sensor extension – better handle storage of sensor deployment information and in situ observations
  Provenance and annotation – capturing more of the context of observations
A more robust “feature model” to better describe the geographic context of observations
Enhanced semantics
Harmonization with WaterML

## Slide 18: Thank you!
CUAHSI
HIS
Sharing hydrologic data
Support EAR 0622374